## Slide 1: Positive Pressure Ventilation: The Basics
Pramita Kuruvilla, M.D.
Critical Care Course
June 2009

## Slide 2: Goals
Introduce the concept of positive pressure ventilation
Introduce the most-commonly used ventilator modes
Discuss patient case and appropriate mode selection
Practice on the ventilators!

## Slide 3: Positive Pressure Ventilation
Includes non-invasive ventilation…
  e.g. facial mask with bagging, BiPAP or CPAP
…and invasive ventilation
  e.g. via endotracheal tube or tracheostomy

## Slide 4: History of PPV
1555: Andreas Vesalius
“…an opening must be attempted in the trunk of the trachea, into which a tube of reed or cane should be put; you will then blow into this, so that the lung may rise again…and the heart becomes strong…”
1930-1950s: Polio Epidemic
  1955 outbreak overwhelmed iron lungs
1950s: First PPV machine in Boston

## Slide 5: Negative Pressure = Normal
Our normal breathing physiology
Diaphragm contracts → negative intrathoracic pressure
Air is sucked in → inspiration
Blood is sucked in to return to the heart → increased venous return / increased preload

## Slide 6: Positive Pressure = Abnormal
Air is pushed in by bag/machine → positive intrathoracic pressure
Cardiovascular effects:
  ↓ preload: blood can’t get sucked in to heart
  ↓ afterload/ ↑ cardiac contractility: pressure squeezes heart during systole
Preload effect predominates if hypovolemic

## Slide 7: Moving on to the Ventilator…

## Slide 8: Ventilator Modes
Volume-based Ventilatory Modes
AC: Assist Control
SIMV: Synchronized Intermittent Mandatory Ventilation
Spontaneous Breathing Modes
PS/PEEP
CPAP

## Slide 9: Case 1 – 68 yo M COPD in ER
COPD “Triage” questions:
    History of intubation? Yes
    Home O2 use? Yes
    Oral steroid use? Yes
PE: RR 40, chest “clear”, falling asleep but can do 1 word answers when aroused
ABG: 7.25/90/<48/35 on 4L ncO2
What interventions, if any, will you do?

## Slide 10: Mode: Assist Control (AC)
Most common initial mode in our ICU
You must fill out vent order form with:
  Mode
  Tidal Volume (usually 10 ml/kg ideal body weight)
  Resp Rate (usually 14-18)
  FiO2 (usually 100 % at first)
  PEEP (positive end expiratory pressure, usually 5cm)
Every breath receives the same tidal volume (Vt) regardless of preset rate.
Extra breaths get the same tidal volume

## Slide 11: PEEP
Positive End-Expiratory Pressure
Air stent: minimum pressure used to “stent” the airway to prevent alveolar collapse/atelactasis
PEEP = ____?____

## Slide 12: Assist Control

## Slide 13: Case 2 – 68 yo M HD#2
Pt is still intubated and on AC mode
FiO2 = 60%
Starting to open eyes intermittently
ABG: 7.55/28/65/30
“Dr, he’s overbreathing the vent; his rate is 40. Do we sedate him more?”
What interventions, if any, will you do?

## Slide 14: Mode: Synchronized Intermittent Mandatory Ventilation (SIMV)
You must order:
  Mode, tidal volume, RR, FiO2, PEEP, and
  Pressure Support (PS)
Ventilator breaths receive full tidal volume only up to the set rate
Extra patient breaths do not get the full tidal volume
Extra breaths get PEEP +/- pressure support

## Slide 15: Pressure Support
Only possible in IMV and spontaneous breathing modes
The extra pressure above the PEEP used to provide additional inspiratory support
Can vary from 0-25 cm

## Slide 16: SIMV

## Slide 17: Case 3 – 68 yo M HD#5
Patient is still on SIMV
He is alert on his daily awakening trial
Follows commands
RR is 25
FiO2 is 30%
What interventions, in any, will you do?

## Slide 18: PEEP and PS/PEEP
Alotaibi, G. Ventilator Graphic Waveforms Tutorial

## Slide 19: And now…
… to the vents